## Slide 1: Media Center Extender UI Remoting And AV Streaming Architecture
Todd Bowra Program Manager eHome Devices Microsoft Corporation

## Slide 2: Media Center Extender Sessions
CON055 – Introduction to Media Center Extender Functionality for Consumer Electronics Devices
CON063 – Media Center Extender UI Remoting and AV Streaming Architecture
CON003 – Adaptation Kit and Certification Program for Implementing Media Center Extender and PlaysForSure

## Slide 3: Session Outline
Recap of Media Center Extender (MCX) technology
MCX UI remoting
  Overview of discovery, configuration, and connection establishment
  UI remoting protocol details
MCX AV streaming
  AV protocol overview
  Advanced AV streaming functionality
  Summary of technology/protocols included in the MCX Platform Adaptation Kit (MCX-PAK)

## Slide 4: What You Will Learn
How Media Center Extender works
How MCX technology ensures a high-quality media playback experience
Which protocols are included in the MCX Platform Adaptation Kit

## Slide 5: What Is MCX Technology?
PC with Windows Vista Home Premium or Ultimate
Network
MCX technology delivers the Media Center experience to
network-connected consumer electronics devices within the home
Consumer electronics device with MCX

## Slide 6: MCX Network Transmission
AV
UI
PC with Windows Vista Home Premium or Ultimate
Media Center Extender
UI and AV information are sent across the network to the MCX device via two separate channels
Network

## Slide 7: MCX UI Remoting

## Slide 8: UI Remoting One-time setup
Before the Media Center UI can be delivered to an MCX device, a trust relationship is created between the PC and MCX
Two one-time steps are involved in creating this relationship
  Discovery
  Configuration

## Slide 9: UI Remoting Discovery
Discovery
PC discovers MCX via Universal Plug and Play (UPnP) for devices
PC checks device compatibility ID to determine if the device contains MCX functionality
If the device is an MCX device, the user receives a presence notification

## Slide 10: UI Remoting Configuration
Trust negotiation
Out-of-band setup key
(entered by user)
On first use, the MCX device displays an eight-digit setup key
The user enters the setup key into the MCX setup wizard on the PC
The wizard performs the following actions
  Installs the MCX device on the PC using PnP-X (Plug and Play Extensions for Network Connected Devices)
  Negotiates a trust agreement between the PC and MCX

## Slide 11: Discovery And Configuration Protocols: UPnP, MSTA
UPnP
  Well-established protocol for discovery
  Used by the PC to discover network-connected devices
Microsoft Trust Agreement (MSTA)
  Used to associate the MCX device with the PC
  Implemented as a UPnP service
  Employs out of band (user-entered) trust code to enable mutual certificate exchange over an insecure network

## Slide 12: UI Remoting Connection establishment
Once a trust relationship is created, the MCX may connect to the PC at any time
Connection establishment is started when the user selects the Media Center experience button on the MCX

## Slide 13: UI Remoting Connection establishment
Application advertisement
The PC advertises a Media Center application Uniform Resource Identifier (URI) to the MCX device
The MCX device validates the authenticity of the advertisement, then connects to the PC
The PC authenticates and authorizes the connection, then remotes the Media Center experience to the MCX device
UI remoting

## Slide 14: Connection Establishment Protocols: MSRX, XSP
Microsoft Remoted Experience Protocol (MSRX)
  Used by the PC to advertise application endpoints to network-connected devices
  Advertisements signed using the PC’s private key – enables devices to verify origin of advertisements
Extender Session Protocol (XSP)
  Used to deliver the Media Center user interface to MCX devices
  Specifically designed for application streaming to consumer electronics devices
  Runs over Transport Layer Security (TLS) for enhanced security

## Slide 15: UI Protocols Summary
 | Included in MCX-PAK | Must be provided by MCX OEM
UPnP |  | 
MSTA |  | 
MSRX |  | 
XSP |  | 
Software support for all UI protocols is included in the MCX Platform Adaptation Kit
Details regarding the MCX Platform Adaptation Kit are provided in the CON 003 session

## Slide 16: UI Remoting Excerpted platform implications
Required by MSTA
  Secure certificate and private key storage
  SHA-1 support
  RSA PKCS1 v2.1 support
Required by XSP
  32-bit graphics support
  Support for full-screen alpha-blended bit BLTs on top of video
Full platform requirements are included as part of the MCX partner documentation

## Slide 17: MCX AV Streaming

## Slide 18: MCX AV Streaming
AV
PC with Windows Vista Home Premium or Ultimate
Media Center Extender
Network

## Slide 19: AV Streaming Scenarios
MCX technology delivers Media Center AV content to network-connected devices within the home; specifically, it enables the streaming of
  Live and recorded TV
    Including HD native digital cable content
  Radio
  Music
  Videos

## Slide 20: AV Streaming Technology
MPEG-2 | ■ | ■ | ■
Windows Media |  | ■ | ■
Windows Media DRM |  | ■ | ■
Fast pre-roll |  |  | ■
Dynamic network monitoring |  |  | ■
Transrating |  |  | ■
The DLNA word mark and logos are owned by DLNA. Other trademarks and trade names are those of their respective owners

## Slide 21: AV Streaming Transport
Play Request
Stream Identifier
AV Samples
Once the user has selected a media stream to play in the Media Center UI remoted from the PC, Media Center sends an identifier for that stream to the MCX device
The MCX device sends a play request to the PC for that stream
The PC delivers the requested stream to the MCX device

## Slide 22: AV Streaming Transport
RTP
  Used to stream TV, FM radio, Windows Media, VC-1, MP3
  Enhanced through use of Quality Windows AV Experience (qWAVE) technology
HTTP
  Used to stream all other formats

## Slide 23: RTP/RTSP Streaming – Details TV, Radio, Windows Media, VC-1, MP3
RTP used for media transport; RTSP used for command and control
Designed for real-time AV streaming
Aligns with Digital Living Network Alliance (DLNA) guidelines
Well-suited to supporting advanced streaming scenarios
  Fast pre-roll
  High-speed fast forward and rewind
  Transrating

## Slide 24: RTP/RTSP Streaming – Enhancements RTCP, qWAVE
MCX sends buffer fullness information to the PC using RTCP receiver reports
qWAVE technology monitors the network fabric
  Measures available network bandwidth and provides notification of congestion
  Diagnoses causes of network performance issues
  Dynamically enables Wi-Fi® Multimedia (WMMTM) prioritization when supported by the network
The PC uses RTCP and qWAVE data to maximize AV quality and performance

## Slide 25: RTP/RTSP Streaming – Startup Fast pre-roll decreases stream startup latency
Device buffer fills at much greater than 1x the play rate; rendering starts 2.75 seconds earlier than standard streaming
Device buffer fills at 1x the play rate, delaying the start of playback until three seconds have elapsed (based upon three second device jitter buffer)
t = 3 seconds
Buffer full
Rendering begins
Time
Network Throughput
Time
Network Throughput
t = 750 ms
Buffer full
t = 250 ms
Rendering begins
Standard pre-roll (non MCX)
MCX fast pre-roll

## Slide 26: RTP/RTSP Streaming – Quality WMM improves AV QoS on congested networks
With WMM:
Video throughput is unaffected when bandwidth is limited because video has higher priority than data traffic
Without WMM:
All streams suffer when network bandwidth is limited
Video
Data
Video
Data

## Slide 27: RTP/RTSP Streaming – Quality Congestion management reduces starvations
The PC monitors network health and MCX buffer fullness
If reduced network capacity is causing device buffers to deplete, the PC transrates the stream to a lower bit-rate
The PC disengages the transrater once device buffers recover

## Slide 28: RTP/RTSP – Protected Content Delivering high-value media to MCX
MCX uses Windows Media DRM for Network Devices (WMDRM-ND) to enable playback of DRM-protected media content
Widespread deployment of WMDRM ensures seamless playback experience
  Many online premium content providers, including PlaysForSure content partners and Media Center Online Spotlight partners, provide music and video content protected using WMDRM
  Media Center protected TV content employs WMDRM (including native digital cable content)

## Slide 29: HTTP Streaming MPEG-1/-2, WAV, OEM-added formats
HTTP is used to stream media formats not streamed via RTP
Aligns with DLNA guidelines
Allows devices to support additional media formats without installing software on the Windows Vista PC
  Enables OEM differentiation via addition of optional decoders to the MCX device

## Slide 30: AV Protocols Summary
 | Included in MCX-PAK | Must be provided by MCX OEM
RTP/RTSP |  | 
RTCP |  | 
qWAVE |  | 
WMDRM-ND |  | 
HTTP for required media formats |  | 
HTTP for optional media formats |  | 
Software support for all required AV protocols is included in the MCX Platform Adaptation Kit
Details regarding the MCX Platform Adaptation Kit are provided in the CON 003 session

## Slide 31: AV Streaming Excerpted platform implications
Required for media playback
  Decoders for MPEG-1, MPEG-2, MP3, AC-3, VC-1, WMV 9, WMA
  High-performance network stack (detailed performance metrics available as part of MCX partner documentation)
Required for WMDRM-ND
  Analog and digital output protection
  Secure private key storage
  AES and RC4 support
Full platform requirements are included as part of the MCX partner documentation

## Slide 32: Call To Action
Attend or review related MCX sessions
  CON055 – Introduction to Media Center Extender Functionality for Consumer Electronics Devices
  CON003 – Adaptation Kit and Certification Program for Implementing Media Center Extender and PlaysForSure
Ensure your platform investments include functionality required to support MCX
E-mail: to obtain addition information about the Media Center Extender partner program
Mcxprtnr @ microsoft.com

## Slide 33: Additional Resources
Related Sessions
  CON074 – Plug and Play for Network Connected Devices
  MED114 – Windows Media DRM Device Ecosystem for Windows Vista
Related Ask the Experts Sessions
  Thursday, May 25, Noon – 1:00 PM
Related Web sites
  Digital Living Network Alliance: http://www.dlna.org/
  PlaysForSure: http://www.playsforsure.com
MCX Partner Program Information
  E-mail:
  Website: http://www.microsoft.com/mcxpartner
mcxprtnr @ microsoft.com

## Slide 34
© 2006 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.